## Slide 1: Ocean Climate Monitoring from Satellite
Key Satellite Products and Measurements

## Slide 2: Sea Surface Temperature (SST)
Technical Terms
SLSTR: Sea and Land Surface Temperature Radiometer - An instrument that measures thermal infrared radiation to determine surface temperature
Radiometer: A device that measures the intensity of radiant energy from Earth’s surface

## Slide 3: Sea Surface Temperature (SST)
Sentinel-3 SLSTR (Copernicus) - European Union’s Earth observation workhorse - Time range: 2016 - present - Frequency: Daily measurements - Resolution: 500m to 1km - Dual-view design reduces atmospheric interference - Used for: Climate monitoring, ocean forecasting1

## Slide 4: Sea Surface Temperature (SST)
MODIS (NASA) - MODIS: Moderate Resolution Imaging Spectroradiometer - A key instrument aboard NASA’s Terra and Aqua satellites - Time range: 2000 - present - Frequency: Daily global coverage - Resolution: 750m - Views entire Earth’s surface every 1-2 days - Measures 36 different spectral bands2

## Slide 5: Ocean Surface Wind Speed
Technical Terms - Scatterometer: A radar instrument that measures ocean surface roughness to determine wind patterns - Altimeter: An instrument that measures distance by timing how long it takes a radar pulse to return from Earth’s surface

## Slide 6: Ocean Surface Wind Speed
Sentinel-6 Michael Freilich (NASA/ESA) - Joint US-European mission named after renowned oceanographer - Time range: 2020 - present - Frequency: 10-day cycle - Coverage: 95% of ice-free oceans - Continues the legacy of Jason satellite series - Primary mission: Sea level rise monitoring34

## Slide 7: Ocean Surface Wind Speed
WindSat (US Navy/NOAA) - Pioneering polarimetric microwave radiometer - Time range: 2003 - present - Frequency: Daily passes - Resolution: 25km grid - First spaceborne polarimetric microwave radiometer - Measures both wind speed and direction without radar5

## Slide 8: Sea Surface Height
Sentinel-6 Michael Freilich (NASA/ESA) - Most accurate sea level monitoring satellite to date - Time range: 2020 - present - Frequency: 10-day cycle - Accuracy: 2.3-3.5 cm - Orbit altitude: 1,336 km - Carries advanced radar altimeter (Poseidon-4) - Also measures atmospheric temperature and humidity67

## Slide 9: Atmospheric Data (Sentinel-6)
Advanced Microwave Radiometer (AMR) measures:
  Water vapor content
  Cloud liquid water
  Rain rate
Data available within hours of collection
Used to correct radar signal delays8

## Slide 10: Notes
1. https://ladsweb.modaps.eosdis.nasa.gov/missions-and-measurements/slstr/
2. https://essd.copernicus.org/articles/13/2111/2021/
3. https://earthobservatory.nasa.gov/images/148461/new-ocean-data-flowing-in
4. https://www.eoportal.org/satellite-missions/copernicus-sentinel-6-michael-freilich
5. https://essd.copernicus.org/articles/13/2111/2021/
6. https://earthobservatory.nasa.gov/images/148461/new-ocean-data-flowing-in
7. https://www.eoportal.org/satellite-missions/copernicus-sentinel-6-michael-freilich
8. https://climate.nasa.gov/news/3052/nasa-us-european-partner-satellite-returns-first-sea-level-measurements/